## Slide 1: Embedded Motion Control 4K450
Lecture 2 – Chapter 4:
Introduction to real-time operating systems
Group 2

## Slide 2: Introduction
Real-time operating systems (RTOS)
A brief history of operating systems
A definition of a RTOS
Scheduler
Objects
Services
Key characteristics
Summary

## Slide 3: History of Operating Systems
Early days: interact with hardware directly
Later: abstraction of underlying hardware
  General-Purpose OS:
    UNIX
    Windows
  Real-Time OS
    VxWorks

## Slide 4: Similarities GPOS & RTOS
Multitasking
Resource Management
Provision of OS services to applications
Abstract hardware from software

## Slide 5: Differences RTOS
Better reliability
Ability to scale up or down
Faster performance
Reduced memory requirements
Scheduling policies tailored for real-time embedded systems
Better portability

## Slide 6: Defining Real-Time OS (1/2)
Program that schedules execution in a timely manner, manages system resources, and provides a consistent foundation for developing application code

## Slide 7: Defining Real-Time OS (2/2)
Every RTOS:
Kernel
Most RTOS kernels:
Scheduler
Objects
Services

## Slide 8: The Scheduler
Provides the algorithms to determine which task executes when.
Scheduable entities
  Kernel objects that compete for execution time
Task or Process
  Independent thread that contains independently scheduable instructions

## Slide 9: Multitasking
The ability to handle multiple activities within set deadlines
Threads might seem to be running
concurrently, however the kernel
is interleaving them sequentially
Based on scheduling algorythm
More tasks = higher requirements

## Slide 10: The Context Switch
Task Control Block (TCB) is data structure for a task
When the kernel switches from one task to another:
  It saves task 1s context info in its TCB
  It loads task 2s info from its TCB, this becomes current
  Context of task 1 is frozen until scheduler switches to task 1 again
Context switch time
  Time it takes for scheduler to switch between tasks
  Relatively insignificant, but excessive switching incurs unnecessary performance overhead

## Slide 11: The Dispatcher
Performs the context switching and changes the flow of execution
Passes the flow of execution (control) through either an application task, through an ISR or through the kernel
Which task should be executed is determined by the scheduling algorithm

## Slide 12: Scheduling algorithms
Scheduling algorithms support 256 priority levels
Preemptive priority-based scheduling
  Scheduling of tasks with
  different priority levels
Round-robin scheduling
  Scheduling of tasks with equal priority levels

## Slide 13: Objects
Building blocks for application development
Taks
  Concurrent and independent threads of execution
Semaphores
  Chapter 7
Message Queues
  Buffer-like data structures

## Slide 14: Services
Application programming interface (API) calls
  Bios
Operations on kernel objects
General:
  Timer management
  Interrupt handling
  Device I/O
  Memory management

## Slide 15: Key Characteristics of an RTOS
Reliability
Predictability
Performance
Compactness
Scalability

## Slide 16: Key Characteristics of an RTOS
Reliability
  Different degrees
  Downtime per year,
  availability
Predictability
Performance
Compactness
Scalability
Number of 9s | Downtime per year
3 Nines (99.9%) | ~9 hours
4 Nines (99.99%) | ~1 hour
5 Nines (99.999%) | ~5 minutes
6 Nines (99.9999%) | ~31 seconds

## Slide 17: Key Characteristics of an RTOS
Reliability
Predictability
  Deterministic RTOS
  Small variance of response times
Performance
Compactness
Scalability

## Slide 18: Key Characteristics of an RTOS
Reliability
Predictability
Performance
  Meet time requirements
  Million Instructions Per Second (MIPS)
  Throughput: rate, bps
  Call-by-call basis
Compactness
Scalability

## Slide 19: Key Characteristics of an RTOS
Reliability
Predictability
Performance
Compactness
  Application design constraints
  Cost constraints
  RTOS memory footprint
Scalability

## Slide 20: Key Characteristics of an RTOS
Reliability
Predictability
Performance
Compactness
Scalability
  Meet application-specific requirements
  Save time and money

## Slide 21: Summary
RTOS vs GPOS
RTOS definition
  Schedule execution, manage system resources, provide foundation
Kernels
  Objects, services, scheduler
Task scheduling
  Preemptive, round-robin
Key characteristics
  Reliable, predictable, high performance, compact, scalable